## Slide 1
PROACTIVE NETWORK MANAGEMENT
Forecasting Jitter, Packet Loss & Latency for Optimal Performance
Data Source : Microsoft Teams Graph API (Mock — enterprise licence cost avoided)
Model : CNN-LSTM with Attention | Unified Multivariate Forecasting
Pipeline : NiFi → Prometheus → Redis → NOC Alerts → Grafana
Maheshwaran K | 2024HT66029 | MTech Cloud Computing and Infrastructure
Supervisor: Rajendra K | BITS Pilani

## Slide 2
01
What Is This Project?
Simple explanation first
The Big Idea — In One Sentence
We watch Microsoft Teams call quality every 5 minutes, learn its patterns using a deep learning model, and WARN the network team BEFORE the call quality goes bad — not after.
😟 TODAY (Reactive)
User complains → Team checks → Fix happens Users already affected. Too late.
😊 OUR SYSTEM (Proactive)
Model predicts spike → Warning sent → Team acts Users never affected. Problem prevented.
🎯 HOW WE DO IT
CNN-LSTM model learns 14 days of Teams call data and forecasts 2 hours ahead.

## Slide 3
02
Problem Statement
Why does this matter?
TODAY — REACTIVE ❌
▸ Issues detected AFTER users complain
▸ Downtime & SLA breaches before action
▸ No early warning for spikes
▸ Each metric monitored separately
▸ NOC team always playing catch-up
THIS PROJECT — PROACTIVE ✅
▸ Forecast degradation BEFORE impact
▸ CNN-LSTM predicts all 3 KPIs together
▸ Early WARNING sent to NOC engineers
▸ Automated Warning → Alert → OK flow
▸ Redis stores spikes for fast retrieval
The 3 KPIs we monitor:
Jitter: Choppy audio in calls
Packet Loss: Missing words / frozen video
Latency: Conversation delay / lag

## Slide 4
03
System Architecture
How all the pieces connect
MS Teams Graph API
Call metrics every 5 min
Apache NiFi
Triggers workflow
Prometheus Time Series DB
14 days history
CNN-LSTM + Attention
Forecast next 2 hrs
Spike Detection
5 methods check data
NOC Alert System
Warn/Alert /OK sent
Supporting Components:
Redis
Stores forecasted spike data (instant retrieval)
Grafana
Visualises 14-day jitter/loss/latency trend dashboards
Mock Teams API
Simulates real MS Teams Graph API (no licence needed)
5 Spike Detectors
Z-Score · IQR Isolation Forest Rolling · Ruptures

## Slide 5
04
Architecture — How It Works
What each part actually does
1
MS Teams Graph API
Every 5 minutes, we ask Microsoft Teams: 'How were your calls?' It gives back Jitter, Packet Loss and Latency for every call. In demo: Mock API generates same data (real API needs expensive Azure licence).
2
Apache NiFi
Think of NiFi as an alarm clock. It wakes up every 5 minutes and says 'Go fetch the latest Teams data now!' It triggers our Python script.
3
Prometheus DB
All the data we collect gets stored here — like a diary of your network. It keeps 14 days of history. Our model reads this diary to learn patterns.
4
CNN-LSTM + Attention Model
This is the brain. It reads the last 2 days of data and asks: 'Based on what happened before, what will happen in the next 2 hours?' CNN finds short patterns. LSTM remembers long history. Attention focuses on what matters.
5
Spike Detection (5 methods)
Five different algorithms check if the forecast shows a problem coming. Z-Score, IQR, Isolation Forest, Rolling Stats, Ruptures — all run together. If ANY of them says 'spike incoming' — we alert. More methods = fewer missed alerts.
6
NOC Alert: Warning → Alerting → OK
WARNING: Model predicts spike in next 2 hours → Email to NOC team to prepare. ALERTING: Real data confirms spike is happening now → Urgent email, take action. OK: Spike gone, network normal again → Email confirms all clear, incident closed.

## Slide 6
05
The CNN-LSTM Model
How the forecasting brain works
Think of it like a weather forecast — but for your network
INPUT
576 time steps (last 2 days of Jitter, Loss, Latency)
CNN Layer
Finds SHORT patterns like a spike 30 min ago or daily peak traffic
LSTM Layer
Remembers LONG history like 'every Monday 6pm network always slows'
ATTENTION
Focuses on the MOST IMPORTANT moments in history
OUTPUT
Forecasts next 24 time steps = 2 hrs Jitter + Loss + Latency
Why unified multivariate? → One model forecasts ALL 3 metrics together, capturing how Jitter, Loss & Latency affect each other
Training: 50 epochs · Batch: 64 · Loss: MSE · Input: 576 steps · Output: 24 steps

## Slide 7
06
Proactive Alert Lifecycle
The 3-stage NOC notification system
Traditional system: User complains → NOC reacts | Our system: Model predicts → NOC acts first
⚠ WARNING
WHEN: CNN-LSTM forecasts a spike 2 hours before it happens
Jitter predicted: 35ms (normal: 8ms) Loss predicted: 2.1% (normal: 0.5%) Latency predicted: 190ms (normal: 45ms)
NOC team gets early warning. They have 2 hours to investigate and prevent the problem.
🚨 ALERTING
WHEN: Real-time data confirms the spike is actually happening
Jitter actual: 35.90ms ⚠ Loss actual: 2.09% ⚠ Latency actual: 192ms ⚠
NOC team confirms the issue. Because of WARNING they are already prepared and acting.
✅ OK
WHEN: Spike subsides and network returns to normal
Jitter back: 6.80ms ✓ Loss back: 0.31% ✓ Latency back: 29ms ✓
Incident closed automatically. All stakeholders notified. No manual update needed.
Key advantage: Zero repeated alerts during ongoing spikes — flag-based deduplication prevents NOC fatigue

## Slide 8
07
Model Validation Results
How accurate is our model?
Forecast Accuracy (RMSE · MAE · MAPE)
Metric
RMSE
MAE
MAPE
Verdict
Jitter (ms)
30.92
22.18
28.0%
✅ Good
Packet Loss (%)
2.13
1.36
High*
✅ RMSE Good
Latency (ms)
20.05
15.44
9.6%
✅ Excellent
* MAPE is unreliable when actual values are near zero (e.g. 0.1% loss). RMSE/MAE are the valid indicators for packet loss.
Anomaly Detection Performance
Precision
0.83
83% of spike alerts are REAL — very few false alarms
Recall
0.89
89% of real spikes CAUGHT — very few missed spikes
What this means:
2 hrs ahead
Model warns NOC before spike hits
5 detectors
Multiple methods reduce missed spikes
Auto OK
Loop closes itself no manual check

## Slide 9
08
Work Done & Plan of Work
Progress and next steps
✅ Completed
✓ MS Teams Graph API mock — exact Graph API schema
✓ Apache NiFi orchestration — 5-minute trigger simulation
✓ Prometheus time-series store — 14-day history ingestion
✓ Data pipeline — cleaning, MinMaxScaler, 3D reshaping
✓ CNN-LSTM with Attention — input 576×3, output 24×3
✓ All 5 spike detectors — Z-Score, IQR, IF, Rolling, Ruptures
✓ Warning → Alerting → OK alert system with deduplication
✓ Redis forecast storage — key: teams_host_jll_forecast
✓ Grafana Prometheus exposition format export
🔜 Next Steps
Model Training
Full 50-epoch training on 14 days real data
Apr 2026
Real-Time Processing
Live spike vs forecasted comparison loop
Apr 2026
Multi-Host Expansion
Extend to multiple Teams tenants
May 2026
Final Viva
Results presentation
Sep 2026

## Slide 10
CONCLUSION
From Reactive to Proactive Network Management
End-to-End Pipeline
MS Teams → NiFi → Prometheus → CNN-LSTM → Redis → Alerts → Grafana
Proactive Alerting
Warning fires 2 hours before spike. Alerting confirms. OK closes loop.
5-Method Detection
Z-Score, IQR, Isolation Forest, Rolling Stats, Ruptures run in parallel.
Mock Data Source
Real MS Teams Graph API schema. Mock used due to enterprise licence cost.
Model Validated
Precision 0.83 · Recall 0.89 · Latency RMSE 20ms · Jitter RMSE 30ms
Future Scope: Multi-host expansion · Automated remediation · Explainable AI for root cause analysis
Thank You — Questions Welcome